V_gs = "gate to source voltage" V_ds = "drain to source voltage" I_d = "Current flowing between drain and source" V_t = "transistor threshold voltage" k' = "transistor transconductance" {W} over {L} = "W to L ratio" Id = uA Linear V_ds < V_gs - V_t : I_d = k'*({W} over {L} *[(V_gs - V_t)*V_ds - {1} over {2}*V_ds^2 ]) Saturated V_ds >= V_gs - V_t :I_d = k'*({1} over {2})({W} over {L}) (V_gs - V_t)^2
ntype k' = 170uA/v^2 & Vt = 0.5v ptype k' = -30uA.v^2 & Vt = -0.5v C_gs = C_ol*W C_ox = E_ox/X_ox ;E = 3.9*( 8.854 x 10^-14 ) "&" X = thickness "in" cm formulas pg 65 – 67 subthreshhold current I_sub = ke^( {V_gs-V_t} over {S/ln10} )[ 1-e^(-qV_ds/kT) ]
formulas pg 77 Saturated V_ds >= V_gs - V_t :I_d = ({1} over {2})k'({W} over {L}) (V_gs - V_t)^2 (12L {0.09um} over {L} )x(3l{0.09um} over {L} )x(4L {0.09um} over {L} )^2 = .42fF 3-------12------|[4]
PAGE 89 SCALING
PG 96 TABLE
MTTF = Ax10^BE e^(E_a/kT); A = const, E_a activation energy, E electric field entensity cm/MV, k const, T absolute Temp
Plotting Ids => use both linear and saturated
Parasitic Resistance 20 𝛌 /3 𝛌 * 7 = 46.67 ohm

CHP3 R_n = 6.47k*ohm ; R_p = 29.6k*ohm t_d = ( -R_n+R_L )C_L*ln0.1 c_l = 0.89fF ex t_d = 2.3*6.47k ohm * 1.78 *10^-15(f)F = 26.4ps R_p inv proportional L/W*R_N
PULLUP CIRCUIT => OR = Parallel AND = Series PULLDOWN is inverted PULLUP ex. Series → Parallel & S → P
AOI 221 => ((A+B)(C+D)(E))'
PULLDOWN = PULLUP in (a+b)' R_PT = L_P over W_P*R_P + L_P over W_P*R_P = R_PT = 2L_P over W_P*4.5R_N = 9L_P over W_P = L_N over W_N = R_NT
(A(b+c))' , consider worst case (separate up and down) 2 series each R_PT = 9L_P over W_P = 2L_N over W_N = R_NT = 4.5L_P over W_P = L_N over W_N
(a+b+c)' 3 pull up 1 pull down = 13.5L_P over W_P = L_N over W_N
delay ex t_d = ( -R_n+R_L )C_L*ln0.1 Assume no R_L = 0; W = 2 L = 6 = -2*2/6*6.47 * ln.1 * 2*n*C_L = 9.93*2*N*C_L
Elmore Delay → S_E = sum from{i = 1} to{n} r( n-i ) C = 1over2RC*n( n-1 ); r = R over n; c = C over n ; R = R_"[ ]" * (L over W); C = c_plate + c_fringe = area * C_"metai1-plate" + pirimeter*C_"metai1-fringe"
ex W = 3𝛌 L=1000 𝛌 𝛌 = 0.09um n = 2 26.67 ohm * 1.106 * 10^-14 * 1 over (2*n) = 7.07 * 10^-14 s
CHP4
Logic Effort → useful for transistor sizing → computes delay of path. Formula1: d=f+p, where d=DelayOfGate, f=EffortDelayRelativeToGateLoad, p=ParasiticDelayOfGateItself. Forumula2: f=gh, where g=LogicalEffortRelativeToGateStructure, h=ElectricalEffortRelativeToGateLoad. Formula3: h=C_out/C_in, where C_out=CapacitanceOfGateLoad (usually next gate along output-input path OR inverter if output is the end), and C_in=CapictanceOfOwnTransistors (drivers or gate in general).
Logical Effort (g) Table for CMOS gates (gate:value, n=# inputs) → Inverter:1, NAND:(n+2)/3, NOR:(2n+1)/3, mux:2, XOR:Undef (1-input), XOR:4 (n=2), XOR:12 (n=3), XOR:32 (n=4). Formula4: d=gh+p. Formula5: D=Sum_i=1_N (d_i) = Sum_i=1_N (g_i h_i) + Sum_i=1_N (p_i), where D=SumOfAllGateDelays, g_i is g for each gate, h_i = h for each gate, p_i = parasitic resistance for each gate (note that transistor = 1 and most other = 2p_i or usually 2). Find C_in by summing delay for each transistor network of gate (parallel choose highest, series sum them up). So a C_i for NAND gate with no other gate inputs and another NAND at its output=1 (here C_in=4 and C_out=4. C_inverter=3).
Combinational Logic Networks → What is fanout? When a gate's pullup and pulldown ratio W/L is too small to drive the gates (have capacitance) connected to its output it runs slowly (term used to refer to this scenario). Speed up fanout by throwing inverter into the mix so that originating gate doesn't drive as many gates. What is path delay? Sum of wire delays along path to gate. What is critical path? Path with largest delay (used for computing logic effort). What is cutset? Set of edges in graph that when removed cause graph to be disconnected. What is timing analysis? Draw graph of gate network to compute path delays. False paths? The result of short circuiting boolean logic (path not always predictable since logic may bypass other check is sufficient inputs attained... waiting on input from other gates... glitching) causes false predictions of path delays.
Sizing Transistors with Logical Effort → NAND example... G=Prod_i=1_N (4/3), F=GBH= (4/3)^3x1x4=9.5, where logic effort is F, G=product of g_i, H=H_i, B=Prod_i=1_n ... branching effort whole path... 1 if no fanout. Branching Effort (b) = (C_onpath+C_offpath)/(C_onpath). OptimumEfforPerStage → f'=cubeRoot(9.5)=2.1.
Logic and Interconnect Design → spanning tree is graph of gates with edges connected to each node (no disconnect). Steiner tree is like spanning tree BUT there are intermediary nodes (new ones aka Steiner points) between the original nodes (man in the middle). Elmore Delay is measurement circuit delay using resistance and capacitance (RC circuits)... start at Vin and follow path to output voltage load... at each resistor we do R0*(C1+C2...+Cn) where R0 is some resistor along path to node we want delay at and C1...Cn is capacitance or Capacitors for each along path away from Vin. Do same for any other Resistor node. Must compute previous Rn along path to Rtarget only. R0(Cx1...Cx2) + R1(Cx1...x2) + Rtarget(Cn). Crosstalk happens when one circuit or channel of system creates an undesired effect in another circuit or channel (wiring problems and path designs) caused by capacitive, inductive, or conductive coupling from on circuit/channel to another... can change output of circuit or alter the time when signals arrive and transition times.
Standard Cell Design → Channel density do vertical line test and count how many paths you intersect... measure of congestion and general indicator of potential crosstalk. Channel routing is when you want to design paths for pins on a system of horizontal and vertical tracks... Left edge routing is... starting from left of view and drawing horizontal segments toward companion pin without track overlap. Pure horizontal segments connecting pin columns. Dog-leg Routing is same as left edge channel routing but allowed to use more than one horizontal segment per net.

Density – connect points then find vertical with greatest number of intersection
Critical path see delay, then apply D = sum g_i*h_i + sum p_i ; h = cout over cin