V_gs = "gate to source voltage" V_ds = "drain to source voltage" I_d = "Current flowing between drain and source" V_t = "transistor threshold voltage" k' = "transistor transconductance" {W} over {L} = "W to L ratio" Id = uA Linear V_ds < V_gs - V_t : I_d = k'*({W} over {L} *[(V_gs - V_t)*V_ds - {1} over {2}*V_ds^2 ]) Saturated V_ds >= V_gs - V_t :I_d = k'*({1} over {2})({W} over {L}) (V_gs - V_t)^2
ntype k' = 170uA/v^2 & Vt = 0.5v ptype k' = -30uA.v^2 & Vt = -0.5v C_gs = C_ol*W C_ox = E_ox/X_ox ;E = 3.9*( 8.854 x 10^-14 ) "&" X = thickness "in" cm formulas pg 65 – 67 subthreshhold current I_sub = ke^( {V_gs-V_t} over {S/ln10} )[ 1-e^(-qV_ds/kT) ]
formulas pg 77 Saturated V_ds >= V_gs - V_t :I_d = ({1} over {2})k'({W} over {L}) (V_gs - V_t)^2 (12L {0.09um} over {L} )x(3l{0.09um} over {L} )x(4L {0.09um} over {L} )^2 = .42fF 3-------12------|[4]
PAGE 89 SCALING
PG 96 TABLE
MTTF = Ax10^BE e^(E_a/kT); A = const, E_a activation energy, E electric field entensity cm/MV, k const, T absolute Temp
HW What W/L is required to make ptype and ntype in terms of saturation drain current: = k'_p/k'_n*3/2 = 170/30*3/2 = 8.5
Plotting Ids => use both linear and saturated
Parasitic Resistance 20 𝛌 /3 𝛌 * 7 = 46.67 ohm

CHP3 R_n = 6.47k*ohm ; R_p = 29.6k*ohm t_d = ( -R_n+R_L )C_L*ln0.1 = 2.3( R_N+R_L )C_L ex t_d = 2.3*6.47k ohm * 1.78 *10^-15(f)F = 26.4ps R_p inv proportional L/W*R_N
HW
PULLUP CIRCUIT => OR = Parallel AND = Series PULLDOWN is inverted PULLUP ex. Series → Parallel & S → P
AOI 221 => ((A+B)(C+D)(E))'
PULLDOWN = PULLUP in (a+b)' R_PT = L_P over W_P*R_P + L_P over W_P*R_P = R_PT = 2L_P over W_P*4.5R_N = 9L_P over W_P = L_N over W_N = R_NT
(A(b+c))' , consider worst case (separate up and down) 2 series each R_PT = 9L_P over W_P = 2L_N over W_N = R_NT = 4.5L_P over W_P = L_N over W_N
(a+b+c)' 3 pull up 1 pull down = 13.5L_P over W_P = L_N over W_N
CHP4
HW